## Slide 1
RESEARCH PROJECT PROPOSAL · PROJECT REVIEW 1
INTERFOG
Stochastic Availability-Aware Fog Orchestration for
Intermittently Powered Energy-Harvesting Nodes
Predicting whether an intermittently powered fog node will remain available long enough to finish a task — and orchestrating execution, checkpointing, migration, or delay accordingly.
Literature coverage: 2024–2026 Web-verified: 09 September 2026

## Slide 2
EXECUTIVE SUMMARY
From current condition to future survival
Conventional fog/edge schedulers decide from current latency, utilization, battery level, or predicted energy. Intermittent-computing systems must also cope with a node losing power before a computation finishes.
INTERFOG treats future node availability as a stochastic quantity — estimating the probability that a node remains operational for the time a task needs — and uses that probability as a primary reliability objective alongside deadline, energy, communication, migration, and checkpoint constraints.
Designed as a research-plus-engineering system: Docker/K3s virtual fog nodes (optionally with physical low-power devices), MQTT telemetry, Python-based modeling, and controlled energy traces.
20
papers reviewed
(2024–2026)
4
policy classes
compared as baselines
7
stress-test
scenarios (S1–S7)
INTERFOG · PROJECT REVIEW 1
02

## Slide 3
PROBLEM STATEMENT
The assumption most schedulers still make
Fog and edge computing place computation closer to data sources — attractive for latency-sensitive IoT workloads. But most scheduling models assume compute nodes remain continuously available during execution.
Energy-harvesting systems violate that assumption: solar, RF, and vibration sources fluctuate; batteries or capacitors deplete; a computation may be interrupted before completion.
“Which execution strategy gives this task the highest probability of successful completion before its deadline, given that fog-node availability itself is uncertain because of intermittent harvested energy?”
WHAT INTERFOG ADDS
Energy-harvesting edge scheduling is already an active field — reliability-aware offloading, energy-aware serverless scheduling, and intermittent checkpointing all exist [R1–R20].
The contribution is not “energy-aware scheduling” in general — it is a specific mechanism where probability of surviving an interruption becomes a first-class scheduling signal.
The scheduler chooses among execute, delay, checkpoint-and-migrate, replicate, or cloud fallback — driven by completion probability under real constraints.
INTERFOG · PROJECT REVIEW 1
03

## Slide 4
CONCEPTUAL ARCHITECTURE
Seven layers, one decision loop
1
Edge / IoT layer
Produces sensing/application tasks; may itself be intermittently powered.
2
Fog-node layer
Distributed compute with heterogeneous energy, CPU, memory, network.
3
Telemetry layer
Energy state, harvesting rate, utilization, queue length, power-cycle history.
4
Stochastic availability model
Maps energy trajectories to a probability of remaining operational.
5
Probabilistic scheduler
Weighs completion probability against latency, energy, deadline, cost.
6
Checkpoint / migration manager
Preserves progress; moves work before predicted depletion.
7
Cloud fallback
High-availability tier when fog completion probability is inadequate.
SEPARATION OF CONCERNS
The architecture keeps three concerns distinct:
Telemetry collection
raw signals from every node
Availability estimation
signals → survival probability
Orchestration decisions
probability → execution strategy
A node with excellent current latency but high interruption risk can be rejected in favor of a slightly slower, far more reliable one.
INTERFOG · PROJECT REVIEW 1
04

## Slide 5
SYSTEM WORKFLOW
End-to-end decision loop
Task
arrival
Telemetry
collection
Energy
prediction
Stochastic
availability
Strategy
selection
Execution
Recovery /
feedback
feeds back to calibrate the availability model
Core decision logic
For every incoming task, INTERFOG estimates execution duration and energy requirement, predicts each candidate node's future energy state, and converts that into an availability probability.
A node with excellent current latency but a high probability of power interruption may be rejected in favor of a slower node with a much higher completion probability.
ILLUSTRATIVE DECISION
Fog-1
latency 20 ms
P(completion) = 0.42
Fog-2
latency 31 ms
P(completion) = 0.91
INTERFOG selects Fog-2: the higher completion probability outweighs the latency penalty.
INTERFOG · PROJECT REVIEW 1
05

## Slide 6
LITERATURE REVIEW
20 papers, 2024–2026 — where INTERFOG sits
5
2026
joint reliability, QoS placement, autonomous scheduling, UAV-MEC
8
2025
checkpointing, mixed-criticality, serverless energy-awareness
7
2024
liveness checkpointing, batteryless design, D2D offloading
ID | Year | Contribution | Gap relative to INTERFOG
R1 | 2026 | Joint delay/reliability-aware EH-MEC offloading & scheduling | Close work — INTERFOG makes survival probability a first-class signal + checkpoint/migration
R7 | 2025 | EDF + energy/timing-aware checkpoint selection (single-core) | Single-node, not distributed fog orchestration
R12 | 2025 | LSTM-driven task merging for intermittent computing | Device-level; INTERFOG operates at the fog orchestration layer
R15 | 2024 | Compiler-level liveness-aware checkpoint optimization | Program-level overhead reduction, not multi-node scheduling
Full matrix (R1–R20) spans EH-MEC offloading, QoS-aware placement, autonomous serverless scheduling, UAV-MEC, checkpointing, and batteryless design — detailed in the proposal document.
INTERFOG · PROJECT REVIEW 1
06

## Slide 7
LITERATURE SYNTHESIS
The identified research gap
EH edge/fog research now covers reliability, service placement, autonomous scheduler selection, renewable-energy prediction, and multi-objective offloading [R1–R14].
Intermittent-computing research separately provides mature checkpointing, persistent state, task merging, and adaptive execution [R7–R8, R12–R13, R15–R16, R19–R20].
The strongest defensible opportunity sits at the orchestration boundary: use a probabilistic model of future node availability to decide execute / wait / checkpoint / migrate / replicate / fall back.
Novelty is stated at the level of the decision mechanism and objective — not as a claim that the constituent technologies are individually unexplored.
DEFENSIBLE NOVELTY POSITION
INTERFOG does not claim that energy harvesting + edge computing, reliability-aware offloading, or intermittent checkpointing is new.
Its contribution is a specific fog-level orchestration mechanism that models energy-driven node availability probabilistically and makes execution / checkpoint / migration decisions using predicted task-completion probability under future power-interruption risk.
INTERFOG · PROJECT REVIEW 1
07

## Slide 8
OBJECTIVES
Eight objectives, from signal to evaluation
1
Develop an energy-state representation from battery, harvesting rate, workload, and power-cycle history.
2
Model future node availability via Markov model, survival model, or calibrated hazard function.
3
Estimate the probability a task completes before the selected node becomes unavailable.
4
Design a scheduler choosing among execution, delay, checkpoint-and-migrate, replication, cloud fallback.
5
Incorporate deadline, energy demand, latency, checkpoint overhead, migration cost, and criticality.
6
Implement a reproducible fog testbed with virtualized nodes and controlled energy traces.
7
Compare against latency-based, resource-aware, energy-aware, and reliability-aware baselines.
8
Quantify completion probability, failures, deadline violations, latency, migrations, energy, recovery time.
INTERFOG · PROJECT REVIEW 1
08

## Slide 9
PROPOSED NOVELTY
From node condition to survival probability
The core novelty: shift from “current node condition” to “probability of remaining operational long enough to finish the task.” A scheduler can reject a node that looks attractive now if its future energy trajectory makes completion unlikely.
STOCHASTIC AVAILABILITY MODEL
P( Aⱼ(t,τ) = 1 | Eⱼ(t), Hⱼ(t:t+τ), Wⱼ(t), Nⱼ(t) )
Aⱼ(t,τ): node j stays operational through [t, t+τ] · E: stored energy · H: harvested-energy behavior · W: workload/resource state · N: network conditions
SCHEDULING OBJECTIVE
maximize αPᴄ − βL − γE − δM − εC − ζV
Pᴄ: completion probability · L: latency · E: energy · M: migration cost · C: checkpoint overhead · V: deadline/SLA violation penalty. Weights are an experimental design parameter, sensitivity-tested.
Why the novelty is defensible
Constituent areas are established — no reliance on “nobody has done EH at the edge.”
Evaluable quantitatively using the same workloads and energy traces across schedulers.
Decision is operational and testable: execute, another node, checkpoint, migrate, replicate, delay, or fall back.
Naturally supports an ablation study isolating availability modeling from prediction and checkpointing.
INTERFOG · PROJECT REVIEW 1
09

## Slide 10
TECHNICAL METHODOLOGY
Six stages, one continuous feedback loop
8.1
Energy-state modeling
Battery SoC, harvesting rate, consumption rate, storage capacity, outage threshold — real traces where possible, synthetic for controlled experiments.
8.2
Availability estimation
Markov chains, HMMs, survival analysis, hazard-rate estimation, or a learned probabilistic predictor — selected via validation experiments.
8.3
Task characterization
Execution time, CPU/memory demand, energy requirement, I/O size, deadline, criticality; long tasks carry checkpointable state.
8.4
Candidate strategy evaluation
Local execution, alternative-node execution, checkpoint-and-migrate, replication, delay, cloud fallback — each scored comparably.
8.5
Execution and migration
Isolated containers; low-overhead checkpoint storage; checkpoint-and-migrate triggers when completion probability drops below threshold.
8.6
Feedback and calibration
Record prediction, action, actual trajectory, actual completion, recovery cost — calibrate probabilities and quantify prediction error.
INTERFOG · PROJECT REVIEW 1
10

## Slide 11
EXPERIMENTAL EVALUATION PLAN
Seven scenarios stress-test the mechanism
ID | Scenario | Condition | Purpose
S1 | Stable harvesting | Moderate battery, predictable energy | Baseline overhead and normal-case QoS
S2 | Energy drought | Sharp drop in harvested energy | Does the scheduler avoid likely-to-fail nodes?
S3 | Workload spike | Rapid growth in task arrival rate | Workload pressure vs. energy risk interaction
S4 | Repeated interruption | Multiple node outages mid-execution | Checkpoint/migration effectiveness
S5 | Heterogeneous fog | Mixed batteries, harvesters, CPUs, links | Generality and fairness of scheduling
S6 | Prediction uncertainty | Noisy or imperfect energy forecasts | Robustness when the predictor is wrong
S7 | Deadline-critical mix | Mixed short/long, critical/non-critical | Completion probability vs. deadline balance
BASELINES COMPARED
Latency-only scheduler
Current-resource scheduler
Residual-energy-aware scheduler
Reliability-constrained scheduler
Random / simple heuristic
Proposed INTERFOG scheduler
INTERFOG · PROJECT REVIEW 1
11

## Slide 12
EVALUATION METRICS
Twelve metrics across reliability, cost, and speed
RELIABILITY
Task completion probability
Task failure rate
Deadline violation rate
Prediction calibration / error
PERFORMANCE
Average latency
P95 latency
Fog-node utilization
Scheduler decision overhead
COST & RECOVERY
Energy consumption
Number of migrations
Checkpoint overhead
Recovery time
INTERFOG · PROJECT REVIEW 1
12

## Slide 13
EXPECTED OUTCOMES
Seven deliverables by end of the project
✓
A working prototype of a distributed fog orchestrator for energy-uncertain nodes.
✓
A validated stochastic node-availability model with documented assumptions and calibration.
✓
A scheduler whose decisions are explainable via completion probability and system cost.
✓
An automated checkpoint-and-migrate mechanism for long-running tasks.
✓
A benchmark suite with repeatable workload and energy scenarios.
✓
A comparative evaluation against multiple baseline policies.
✓
A research-paper-ready formulation of problem, algorithm, methodology, and novelty claim.
INTERFOG · PROJECT REVIEW 1
13

## Slide 14
FEASIBILITY & IMPLEMENTATION STACK
Achievable with student-level infrastructure
Infrastructure
Docker · Kubernetes/K3s · Linux
Messaging
MQTT · optional gRPC/REST
Monitoring
Prometheus · Grafana
Modeling
Python · NumPy · pandas · scikit-learn · optional PyTorch
Storage
PostgreSQL / SQLite / Redis
Energy data
Real EH traces where available · controlled synthetic traces
Hardware (optional)
Raspberry Pi · low-power MCU · EH demonstrator
Experiment control
CPU/memory constraints · process suspension · network emulation
FEASIBILITY STRATEGY
No large physical fog laboratory is required.
Emulate 10–50 heterogeneous fog nodes using containers, then connect one or more real low-power devices for demonstration.
“Power loss” is represented in the emulator via an energy trace or a calibrated outage process — preserving research realism while keeping the project achievable.
INTERFOG · PROJECT REVIEW 1
14

## Slide 15
RESEARCH QUESTIONS & HYPOTHESES
Four questions, four testable hypotheses
RESEARCH QUESTIONS
RQ1
Can future energy state be converted into a useful probabilistic estimate of fog-node availability?
RQ2
Does completion-probability scheduling reduce task failures under intermittent power vs. current-state scheduling?
RQ3
When does checkpoint-and-migrate outperform immediate migration, delay, or cloud fallback?
RQ4
How sensitive is the scheduler to forecast error, checkpoint overhead, and migration latency?
HYPOTHESES
H1
Stochastic availability-aware scheduling increases completion probability vs. latency-only and current-resource baselines.
H2
Proactive checkpoint-and-migrate reduces deadline violations for long-running tasks under high outage probability.
H3
Completion-probability-aware scheduling reduces unnecessary migrations vs. a fixed energy-threshold policy.
H4
The benefit remains measurable under imperfect forecasts, provided the probability model is calibrated.
INTERFOG · PROJECT REVIEW 1
15

## Slide 16
Thank you
Questions and discussion — Project Review 1
INTERFOG — Stochastic Availability-Aware Fog Orchestration for Intermittently Powered Energy-Harvesting Nodes